## Slide 1: CPE 490 Embedded Systems
Professor Barlow
Prayer
Syllabus
Class Schedule
Blackboard

## Slide 2: dsPIC33 high-Performance 16-bit Digital Signal Controllers Data Sheet
The data sheet for this part is 350 pages
It is essential that you get a hard copy of the data sheet to use in the lab and on exams.
The data sheet can be purchased for $10 from Mrs. Mlynarski in the engineering office
You will be refunded the $10 if you bring the data sheet back at the end of the semester
Newest revision ‘D’ is posted on Blackboard (hard copy is ‘C’ can be corrected to ‘D’)
Notes: To correct consult page 351 in revision ‘D’

## Slide 3: Why CPE 490 ???
Learn how to interface to and program a modern, powerful embedded system with Digital Signal Processing (DSP) functions
Learn how to program an embedded system using C code
Learn about Real Time Operating Systems.
Learn about peripherals: LCD, DAC, ADC, and DMA
Notes: Liquid Crystal Display LCD
Digital to Analog Converter (DAC)
Analog to Digital Converter (ADC)
Direct Memory Access (DMA)

## Slide 4: Keys to Success
Come to class
Get a good C code text
Stay up with labs (Labs and Semester Project is 50% of your grade)
Work on labs outside of lab time
Read the data dsPIC33 data sheet
Own you code, practice good debugging techniques
  Write code in small modules test them as you go
  Document your code
  Isolate your problem
Notes: See blackboard for article on good debugging practices

## Slide 5
The Embedded System - What Disciplines does it Involve?
Embedded Systems
Electronics
Electric Motors &
Computer Architecture
Software Engineering
Integrated Circuit
Design
Digital
Analogue
Electronics
Actuators
Sensors and
Measurements
Control
Engineering
Data
Communications
Notes: Embedded systems will continue to be important. Because of there ability to control things we will continue to seem them in optimization of many products, especially ones that can benefit from optimization of energy use.
A huge area is the ability to put internet connectivity into many different products like phones, music players, and the ability for a user to check up on embedded systems like lighting , environmental, and security control.

## Slide 6: Outline of Course
The C language and how to use it in an embedded system
16 bit microcontroller with (DSP) functions
  Hardware multiplier
  Interrupts
  Non volatile memory
Real Time Operating System (RTOS)
Analog to Digital interface
Direct Memory Access
Connectivity Networking

## Slide 7: Embedded systems overview
Computing systems are everywhere
Most of us think of “desktop” computers
  PC’s
  Laptops
  Mainframes
  Servers
But there’s another type of computing system
  Far more common...

## Slide 8: Embedded systems overview
Embedded computing systems
  Computing systems embedded within electronic devices
  Hard to define. Nearly any computing system other than a desktop computer
  Billions of units produced yearly, versus millions of desktop units
  Perhaps 50 per household and per automobile
Computers are in here...
and here...
and even here...
Lots more of these, though they cost a lot less each.
Notes: In bold is the authors definition of an embedded system.
The author projects maybe 300 by 2004 (book is dated)
Several billion embedded microprocessors units were sold compared to a few 100 million desktop units

## Slide 9: A “short list” of embedded systems
And the list goes on and on
Anti-lock brakes
Auto-focus cameras
Automatic teller machines
Automatic toll systems
Automatic transmission
Avionic systems
Battery chargers
Camcorders
Cell phones
Cell-phone base stations
Cordless phones
Cruise control
Curbside check-in systems
Digital cameras
Disk drives
Electronic card readers
Electronic instruments
Electronic toys/games
Factory control
Fax machines
Fingerprint identifiers
Home security systems
Life-support systems
Medical testing systems
Modems
MPEG decoders
Network cards
Network switches/routers
On-board navigation
Pagers
Photocopiers
Point-of-sale systems
Portable video games
Printers
Satellite phones
Scanners
Smart ovens/dishwashers
Speech recognizers
Stereo systems
Teleconferencing systems
Televisions
Temperature controllers
Theft tracking systems
TV set-top boxes
VCR’s, DVD players
Video game consoles
Video phones
Washers and dryers

## Slide 10: What is a Embedded system?
Single-functioned
  Executes a single program, repeatedly
Tightly-constrained
  Low cost, low power, small, fast,
Reactive and real-time
  Continually reacts to changes in the system’s environment
  Must compute certain results in real-time without delay
Notes: What would a cell phone be.

## Slide 11: What is a Embedded system?
RTOS not GPOS
  VxWorks, Salvo, QNX, not Windows or Linux
Failures cost more
  Safety systems
Extreme environments
Notes: What would a cell phone be.

## Slide 12: C Programming Language
C was first invented by Dennis Ritchie in 1972 it was used to write the operating system UNIX on a DEC PDP 11 at the Bell Labs, in New Jersey, USA.
Its first publicly available documentation was in a publication by Brian Kernighan and Dennis Ritchie in 1978. This became so well known that it is often called the “K&R” version.
Notes: In 1978, Brian Kernighan and Dennis Ritchie published the first edition of The C Programming Language

## Slide 13: C Programming Language
In 1989 a version of C was adopted by the American National Standards Institute (ANSI), as standard X3.159-1989. It is important to recognize this standard, as it is the one that the Microchip MPLAB XC16 compiler is based upon. It became very widely recognized and adopted, and one finds many references to “ANSI C”.
In 1990, the International Organization for Standards (ISO) adopted the same version as an International Standard, with amendments made in 1995 and 1999. The 1999 version contains extensions which are not implemented in many compilers targeted at embedded systems.

## Slide 14
The Problem of Programming, and Programming Options
What options do we have for programming a microcontroller?
Use Machine Code
Use High Level Language
Use Assembler
11010010
01010010
11010101
01001011
01100011
....
Shall I
compare
thee
to a
summer
day........?
Notes: A microprocessor has a very limited language …. Its instruction set. In the case of the PIC16 only 35 instructions. Worse, the instruction must be in binary, or machine code for the processor to understand the instruction.
A person is a verbose, variable, abstract thinker
The problem is how to get the two to get the two to think in the same way. This bridge is made through the software languages we choose to use. We will consider three options

## Slide 15: Middle Level Language
Above assembler, provides ability to develop high level constructs that are already defined in a high level language.
BUT C does not abstract the machine hardware from the programmer.
  Gives ability to manipulate down to the bit and byte level, and allows ability to use physical addresses
  You can build routines to interface with peripherals making it possible to use in small embedded systems
  The programmer still has control over embedded resources like memory space

## Slide 16: Why C?
Minimal language – only 32 keywords
Since it is lower level and closer to assembly language; easier to write a compiler. Most processors have a C compiler
Fast efficient code, taking away the need to optimize portions of the code in assembler.
Portable – if you write it for one hardware target, fairly easy to port it to another target.
Notes: Indeed assembly languages are now designed to be C like (feature stated in dsPIC data sheet)

## Slide 17: Structured Language
The ability to organize your code in blocks or functions.
Subroutines with local variables (absence of Global variables)
Loop constructs like while, do/while, and for
The avoidance of goto
Notes: No spaghetti code!

## Slide 18: Compiled vs. Interpreted
The C language source code is compiled and made into hex or machine code.
Interpreted languages like BASIC or Java (some forms) execute at run time .

## Slide 19: Reading Assignment
In the data sheet posted on blackboard for this lecture read:
  Section 1 (overview)
  Section 3 (CPU)
  Section 4 (memory organization)
  Section 11 (I/O ports)
For next Thursday look over
  Section 12 (Timer 1)

## Slide 20: Anatomy of a C program
Free form programming
  The column that a statement begins in has no meaning to the compiler (compare to assembler labels in column 1)
Comments
Declarations
Statements
White Space

## Slide 21
/***************************************************************************
Example1.
Introductory Example of C Programming, with dsPIC Series Microcontroller.
16-bit value output by Port B is continuously incremented.
WDB 01.14.13 Tested 01.14.13
***************************************************************************/
//Include 33FJ256GP710A header file, for all processor-specific declarations
#include <p33FJ256GP710A.h>
unsigned int counter; //specify counter as unsigned character
void main (void) //main function starts here
{
TRISB = 0; // initialise all bits of PORTB as output
counter = 1; //counter value is initialised to 1
AD1PCFGL = 0xFFFF; // turn off analog function on portb I/O pins
while (1)
{
PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1; //Increment counter
}
}
Example C Program for dsPIC Series PIC Microcontroller

## Slide 22: Comments /* ….. */
Start with /* end with */
Can be multiple lines in between
No problem with free space
// used for a single line comment
Be generous with comments
/***************************************************************************
Example1.
Introductory Example of C Programming, with dsPIC Series Microcontroller.
16-bit value output by Port B is continuously incremented.
WDB 01.14.13 Tested 01.14.13
***************************************************************************/
//Include 33FJ256GP710A header file, for all processor-specific declarations

## Slide 23: Declarations
Create program elements and indicate properties
All variables and functions must be declared
Usually appear at the beginning of the program
unsigned int counter; //specify counter as unsigned character

## Slide 24: Statements
Where the action takes place
Perform mathematical or logical operations and establish program flow
Every statement ends in a semicolon
TRISB = 0; // initialise all bits of PORTB as output
counter = 1; //counter value is initialised to 1
AD1PCFGL = 0xFFFF; // turn off analog function on portb I/O pins
Notes: The examples are a mathematical assignment statement or and expression statement

## Slide 25: Code Blocks
A block of declarations and statements
Contained within curly brackets {}
Notice the absent of semicolon
Can be nested, use tabs to set each block vertically in its own column
while (1)
{
PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1; //Increment counter
}

## Slide 26: Use of Space
Blank spaces and blank lines are ignored by the compiler.
while (1)
{
PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1; //Increment counter
}
while (1){PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1;} //Increment counter
OR