## Slide 1: CPE 490 Embedded Systems
Lecture 3
C language Chapter 14.2.2-14.2.6
  Comments, Declarations, Statements, White space, Key Words
  Functions
  Data type and storage

## Slide 2: Anatomy of a C program
Free form programming
  The column that a statement begins in has no meaning to the compiler (compare to assembler labels in column 1)
Comments
Preprocessor Directives
Declarations
Statements
White Space

## Slide 3
/***************************************************************************
Example1.
Introductory Example of C Programming, with dsPIC Series Microcontroller.
16-bit value output by Port B is continuously incremented.
WDB 01.14.13 Tested 01.14.13
***************************************************************************/
//Include 33FJ256GP710A header file, for all processor-specific declarations
#include <p33FJ256GP710A.h>
unsigned int counter; //specify counter as unsigned character
int main (void) //main function starts here
{
TRISB = 0; // initialise all bits of PORTB as output
counter = 1; //counter value is initialised to 1
AD1PCFGL = 0xFFFF; // turn off analog function on portb I/O pins
AD2PCFGL = 0xFFFF; //two ADCs have access to lower 16 analog channels
while (1)
{
PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1; //Increment counter
}
}
Example C Program for dsPIC Series PIC Microcontroller

## Slide 4: Comments /* ….. */
Start with /* end with */
Can be multiple lines in between
No problem with free space
// used for a single line comment
Be generous with comments
/***************************************************************************
Example1.
Introductory Example of C Programming, with dsPIC Series Microcontroller.
16-bit value output by Port B is continuously incremented.
WDB 01.14.13 Tested 01.14.13
***************************************************************************/
//Include 33FJ256GP710A header file, for all processor-specific declarations

## Slide 5: Preprocessor Directives
Any time # is used it is to denote a preprocessor directive.
These statements do not make code directly
#include is used to link a header file to this file
All defined variables in the header can be used in this program.
The provided headers allow you to reference SFR registers directly
/*Include 33FJ256GP710A header file, for all processor-specific declarations */
#include <p33FJ256GP710A.h>

## Slide 6: Declarations
Create program elements and indicate properties
All variables and functions must be declared
Usually appear at the beginning of the program
unsigned int counter; //specify counter as unsigned character

## Slide 7: Statements
Where the action takes place
Perform mathematical or logical operations and establish program flow
Every statement ends in a semicolon
TRISB = 0; // initialise all bits of PORTB as output
counter = 1; //counter value is initialised to 1
AD1PCFGL = 0xFFFF; // turn off analog function on portb I/O pins
Notes: The examples are a mathematical assignment statement or and expression statement

## Slide 8: Code Blocks
A block of declarations and statements
Contained within curly brackets {}
Notice the absent of semicolon
Can be nested, use tabs to set each block vertically in its own column
while (1)
{
PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1; //Increment counter
}

## Slide 9: Use of Space
Blank spaces and blank lines are ignored by the compiler.
while (1)
{
PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1; //Increment counter
}
while (1){PORTB = counter; // Move 'counter' value to Port B
counter = counter + 1;} //Increment counter
OR

## Slide 10: C Key Words
Keywords can not be used as user defined names
    auto double int struct
    Break else long switch
    case enum register typedef
    char extern return union
    const float short unsigned
    continue for signed void
    default goto sizeof volatile
    do if static while
Notes: Appendix 6 in your text book lists all key words with definitions

## Slide 11: Functions In C
Functions can have multiple inputs called parameters or arguments
Only one return variable is allowed
A function may call a function
Function
Parameter 1
Parameter 2
Parameter 3
Parameter N
.
.
.
Output

## Slide 12: General Form of a Function
Type-specifier function_name(parameter declarations)
{
body of function
}
Type-specifier: declares the type of value the function will return. The default is integer not void
Parameter declarations: comma separated list that looks like
  (type varname1, type varname2, ..., type varnameN)
Notes: Parameter list can be blank but parenthesis remain. When the function is called each variable name will be initialized to called value.

## Slide 13: Function Isolation
Functions are isolated both code and data wise from any other function
Code in one function can not be jumped to with a GOTO statement outside of the function
If a local variable is declared with the same name as the global variable, the local will be used in the function it is declared.

## Slide 14: Scope Rules
Local Variables: a block of C code is defined by the {} brackets. Variables declared in a block only have meaning within that block.
Formal Parameters: These are the passed arguments when the function is called. Other than having a passed value they behave like any other local variable. That is the variable passed is a local copy the variable itself does not change value if it is changed in the program
Notes: Local variable are not available to other blocks that exists outside of the block they are declared in. So a variable declared in a function is only available in that function. The variable is created when the block is entered and it is destroyed upon exit (unless you declare it static) . If you want to pass a data variable back when you return this is type specifier that you declared the function to have.

## Slide 15: Scope Rules
Global Variables
  Known through out the program can be used by any piece of code.
  Static they hold there value as long as the program is running
  Declared outside of all functions (including main())
Notes: Remember a variable must be declared before it is used so best to declare global variables at the top of the program

## Slide 16: Problems with Global Variables
They take up memory the entire time your program is executing.
Using a global were a local variable will do makes a function less general because it relies on something defined outside of itself. (Code reuse is hindered)
Using a large number of global variables can lead to program errors because of unanticipated side effects
Notes: If a program is large any piece of code can change the global variable. You might not remember that a piece of code does this, causing a bug that can be difficult to find.
Remember the point of structured code is to compartmentalize the code and data, global variables are in violation of this concept.

## Slide 17: A Multiply Function
General
mul(int x, int y)
{
return (x*y);
}
/* This function can be used to multiply any two integers */
Specific
int x, y ;
mul()
{
return(x*y)
}
/* This function can only be used on global variables x, and y. */

## Slide 18: main ()
main is a function, and all C programs begin with a call to main. It is required to be present
main declaration can be any where in source code file but it is common to make it the first code statement
In an embedded system some initialization must be done before main is called. This code is inserted by the linker and is known as c0 code.
Notes: You saw c0 code in the last lab.

## Slide 19: Main is a Function
Return Type
Function Name
Argument(s) Type(s)
Opening of function
Close of function
void main (void) //main function starts here
{
...
(body of function goes here)
...
}
X
Mistake in book returns an int
int
Notes: No type declaration will also work as the default return type is integer
If you try to put void in place the following will be given:
main.c:14: warning: return type of 'main' is not 'int‘
If you don’t put any return type you will get :
main.c:14: warning: return type defaults to 'int‘
In fact main can accept arguments for the command line that calls the compiler, it returns a 0 if a standard exit of the subroutine has occurred.

## Slide 20: The End of main()
What happens when the closing bracket (}) of the main function is reached?
  A processor reset is executed (the dsPIC33 has an instruction RESET)
  c0 code runs again and main is called again
Inefficient to keep running the c0 initialization code so we should not write code that allows main to encounter the closing bracket.

## Slide 21: Variables in C
Variables in C must be declared before they are used.
They have 4 attributes
  Name
  Type
  Value
  Storage Location

## Slide 22: Variable Names
Variable names have their first 31 characters as significant.
They are case sensitive
They may start with a letter or an underscore, after that any combination of underscore, letter or digits can be used.
Don’t use any C keywords or use standard functions names (like printf).

## Slide 23: Variable Type
Of the form: type variable_list; ex int c,d;
Bit size is compiler (processor) dependent
The Integer Variable types are as follows:
Notes: Long means a long integer that is takes up 32 bits
Void (not shown) is used for example to describe that a functions returns no data.
In an embedded device RAM is precious so only declare what you need for example if i is a counting variable that never goes past 10 declare I as a char.
Data types are defined in the MPLAB XC16 Compiler Users Guide.

## Slide 24: Variable Type
The Floating Variable types are as follows:
Notes: All floating point numbers are signed , in the IEEE754 standard the MSB is the sign bit.

## Slide 25: Variable Initialization (value)
Done at declaration with equal sign, ex.
  int first = 42;
Global variables are initialized only at the start of the program
Local variables are initialize each time the function is entered (can save a slight amount of time)

## Slide 26: Variable Storage Location
Keyword precedes the type indicator Example:
extern int first;
Auto – default storage class specifier, that declares the variable local. Rarely used since it is the default.
Extern – The variable is global and declared in some other file that will be linked in

## Slide 27: Variable Storage Location Cont.
Static – a local variable that retains it value between function calls.
  If used on a global variable then the variable is only known to the file it is declared in
Register – The variable should be stored in a processor register for quick use.
Notes: Static is the same as global except for the scope rule. Like global if static only initialized once