## Slide 1: CPE 490 Embedded Systems Lecture 20
Data acquisition and manipulation (Wilmshurst Text Chapter 11)
dsPIC33F256GP710A ADC system

## Slide 2
The Sample and Hold Circuit
Because most ADCs work better converting a stationary voltage, a Sample and Hold circuit is commonly used. In this type of circuit a capacitor is charged from a source which inevitably has some resistance. Further resistance comes from internal resistance of the solid-state switch used in the S&H, and/or in the multiplexer. Therefore the capacitor takes finite time to charge, with a charging characteristic as shown.
A Simple Form of Sample and Hold Circuit
Charging Characteristic of Sample & Hold
Notes: So how close to Vs must you get, lets say to ½ bit. So an 8 bit converter is 1/255* 1/2 = .196% or X = .9980. This gives a t of RC 6.238

## Slide 3: A Sample and Hold Circuit
Notes: Just an example of an external S/H.

## Slide 4: Problem
A pressure sensor has 250 Ohms of output resistance. A sample and hold circuit uses a .1 uF capacitor. The sample hold circuit feeds a 10 bit ADC. How long should sampling take to ensure not injecting more than ¼ bit of error?

## Slide 5: Successive Approximation A/D
Notes: This is the type of A/D convertor in the dsPIC

## Slide 6
The ADC accepts an input voltage that is infinitely variable, and converts this to one of a fixed number of output values. An example ADC conversion characteristic is shown, where the input voltage is represented on the horizontal axis, and digital output on the vertical.
For an n-bit ADC, the maximum output value will be (2n – 1). For example, for an 8-bit ADC, the maximum value will be (28 – 1), or (256 – 1), i.e. 255 decimal or 11111111 binary.
The Analog to Digital Converter (ADC)
...001
010
011
100
V
max
Digital
Output
Analogue
Input
0
(2 - 1)
n
(2 - 2)
n
0
Input Range
Min 0 V = Code 0
Max Vmax = Code 2n – 1
Resolution = Vmax /(2n – 1)
Code = D = e/Vmax (2n – 1)
Notes: Notice that the change to a code will ideally happen in ½ of the interval of resolutions
Also note that the text has the resolution wrong when it states it is V/2^N

## Slide 7: ADC
ADC
Converts its
Analog
Input to a
Digital Output
Voltage
Reference
Digital
Output
CPU
Control
Output
Result
Conversion
The voltage reference is the standard that is used to find ADC values. The ADC can only be as accurate the voltage reference
The conversion speed of the ADC puts a limit on the bandwidth of the signal you are measuring.
Digital interface between processor and ADC can be parallel or serial (SPI, I^2C)

## Slide 8: Location of ADC
Two choices:
  Integrated in the microcontroller
  Separate with some type of interface to the processor
A microcontroller is an electrical noisy place.
  Remember many (10s of thousands) transistors change on every clock edge
  Hard to get better than 10 bit performance
I separate ADC can be isolated on the PCB to be in a quiet zone.

## Slide 9: Making Integrated ADCs Quiet
Give separate supply and ground supplies
Do conversion between clock edges
Even so hard to get better than 8 or 10 bit ADC resolution

## Slide 10
Typical Timing Requirement of one A to D Conversion
Configure & enable ADC
Select
Multiplexer
input
Delay for signal acquisition
Start Conversion
Delay for conversion
to complete
Read Data
“Sample” Input Signal
“Hold” Input Signal
These stages merge
if
multiplexer
forms
part of S&H

## Slide 11: dsPIC33FJ256GP710A ADC
There are 2 SAR ADCs: ADC1, and ADC2
Each can be configure for 12 or 10 bit operations
Up to 32 analog input pins
The chip is capable of sampling 1.1 million times a second in 10 bit mode, 500 thousand times a second for 12 bit mode
  Engineering tradeoff resolution for speed
Notes: 1.1 million times a second is period of 909 ns
500 thousand times is a period of 2 useconds

## Slide 12: dsPIC33FJ256GP710A ADC
Four unipolar differential sample and hold amplifiers
External voltage reference input pins
Simultaneous sampling of up to four input pins
Auto scan mode
Selectable trigger sources
DMA
Notes: Channenl Scan mode can be enabled for Channel 0 . Any subset of the analog inputs can be selected by the user application.

## Slide 13
12 bit mode only uses S/H Channel 0
This is a model of ADC1 it can use all 32 inputs.
ADC2 is not shown it can use the first 16 analog inputs

## Slide 14: Differential Vs Single Ended
If the signal you want to read is referenced to a common ground then single ended is possible

## Slide 15: Sampling Mode
Up to 4 channels can be sampled simultaneously
Simultaneous sampling can be important in control and power calculations.
Notes: You can configure how many sample and hold channels are going to be active for any mode. Choices are:
CH0 Only or
CH0, and CH1 or
CH0, CH1, CH2, and CH3
Remember in 12 bit mode there is only one sample and hold

## Slide 16: ADC SFRs
ADxCON1 – ADxCON4 (various control #4 allocates DMA memory)
ADxCHS123: ADCx Input Channel 1, 2, 3 Select Register
ADxCHS0: ADCx Input Channel 0 Select Register
AD1CSSH: ADC1 Input Scan Select Register High
ADxCSSL: ADCx Input Scan Select Register Low
AD1PCFGH: ADC1 Port Configuration Register High
ADxPCFGL: ADCx Port Configuration Register Low
Notes: The ADxPCFGH registers are to select the digital or analog function of the 32 ADC pins

## Slide 17: Overview of Sample and Conversion

## Slide 18: Sampling Initiation and Ending
Notes: To start manual sampling set the SAMP bit in the ADxCON1 and then go to hold by clearing the bit.
Caution there is a finite amount of sampling time that must be observed 3 Tad for 12 bit mode 2 Tad for 10 bit mode.

## Slide 19: Conversion Time

## Slide 20: Conversion Initiation

## Slide 21: Manual Sample Manual Conversion
ASAM = 0, SSRC = 000

## Slide 22: Auto Sample and Manual Convert
ASAM = 1, SSRC = 000 Sampling starts auto-matically right after conversion
Notes: The only difference from manual / manual is that you don’t have to set the SAMP = 1

## Slide 23: Auto Sample and Auto Convert
ASM = 1, SSRC = 111 Cont. periodic sampling
SAMC<4:0> select the sampling period conversion occurs after sampling

## Slide 24: Auto Sample and Triggered Convert
ASM=1, SSRC = 001,010,011
Sample starts after conversion ends
Notes: 001 event external interrupt (INT0)
010, 100 Timer Interrupt Trigger
011 Motor Control PWM Special Event Trigger

## Slide 25: Sampling Mode Details
Notes: Can’t do 12 bit simultaneous samples.

## Slide 26: 2 Channel Simultaneous Sampling

## Slide 27: 4 Channel Simultaneous Sampling

## Slide 28: Calculation of Total Time to Sample