## Slide 1: CPE 490 Embedded Systems Lecture 7
Structures and unions (17.8)
Type Conversions
Casting
Prototyping (15.3)
Bit wise operations (15.1)

## Slide 2: Single Dimensional Arrays
Declaration is: type var_name[size];
Where type is as detailed above.
Var_name follows the naming convention
Size represents the number in the array.
Example
int i[10]; // declares i as an array of 10X16 integers

## Slide 3: C Structures
Structure – a collection of variables referenced under one name.
Conglomerate of data types that are logically linked together.
Like a record
Must be declared first than instances can be created.

## Slide 4: C Structures
Structure – a collection of variables referenced under one name.
Has the form of
struct struct-type-name {
type element_name_1;
type element_name_2;
.
.
.
type element_nameM;
} structure-variables;
Notes: You can eliminate the struct-type-name, if you declare your variables structure-variables but you can not then use the defined type declaring any other variables. In contrast you give the structure a name but not in this statement declare any variables. Later you could declare “struct struct-type-name examplevariable;
An array can be one of the elements. Also structures can be used to make an array of structures.

## Slide 5: Structure Example
struct inv_type {
  char item[40]; /*name of item*/
  double cost; /*cost */
  double retail; /* retail price */
  int on_hand; /* amount on hand */
  int lead_time; /*number of days before resupply*/
  };
  */ later in the program*/
  struct inv_type inv_var ;
Notes: Lets you a collection of related items as one logical unit.

## Slide 6: Structure in Memory
Variable | Memory Space
item | 40 bytes
cost | 4 bytes
retail | 4 bytes
on_hand | 2 bytes
lead_time | 2 bytes
inv_var

## Slide 7: Accessing and Element in a Structure
Prototype: structure_varname.element_name
The following will allow assignment to the inventory cost of our last example
inv_var.cost = 10.39;

## Slide 8: Defining and Declaring
struct inv_type {
  char item[40]; /*name of item*/
  double cost; /*cost */
  double retail; /* retail price */
  int on_hand; /* amount on hand */
  int lead_time; /*number of days before resupply*/
  }inv_varA, inv_varB, inv_varC;

## Slide 9: Defining and Declaring Once
struct {
  char item[40]; /*name of item*/
  double cost; /*cost */
  double retail; /* retail price */
  int on_hand; /* amount on hand */
  int lead_time; /*number of days before resupply*/
  }temp;

## Slide 10: Bit Fields
Bit fields can be declared and used based on structures.
A bit field is really just a special type of structure that defines how long in bits each element is to be.
Each bit field will have a type of int, unsigned or signed. If the bit field is just one bit it should have a type of unsigned.

## Slide 11: Prototype Structure with BitField
struct struc-type-name{
type name1 : length;
type name2 : length;
.
.
.
type nameN : length;
}

## Slide 12: Example
struct tagPORTABITS {
unsigned RA0:1;
unsigned RA1:1;
unsigned RA2:1;
unsigned RA3:1;
unsigned RA4:1;
unsigned RA5:1;
unsigned RA6:1;
unsigned RA7:1;
unsigned :1;
unsigned RA9:1;
unsigned RA10:1;
unsigned :1;
unsigned RA12:1;
unsigned RA13:1;
unsigned RA14:1;
unsigned RA15:1;
} PORTABITS;
Notes: Note this comes from the header file. There is a typedef before the struct statement. This changes things to mean the structure type tagPORTABITS is not called PORTABITS for short hand. We will see this in a few slides. Without the typedef PORTABITS is an instance of the tagPORTABITS type.

## Slide 13: C Union
A union is a memory location that is shared by several different types of variables at different times.
For example
union union_type {
int i;
char ch;
};
union union_type u_var;
Definition
Instance
Notes: It’s not possible for the union to hold and int and a char at the same time, but your program is free to treat the information in the union as an integer or a character at any time.

## Slide 14: Memory Allocation of Union
Byte 1 | Byte 0
i
ch
Example of using the created instance
U_var.ch = ‘A’;

## Slide 15: Example of Structure and Union
union {
struct {
unsigned :1;
unsigned TCS:1;
unsigned TSYNC:1;
unsigned :1;
unsigned TCKPS:2;
unsigned TGATE:1;
unsigned :6;
unsigned TSIDL:1;
unsigned :1;
unsigned TON:1;
};
struct {
unsigned :4;
unsigned TCKPS0:1;
unsigned TCKPS1:1;
};
} T1CONBITS;
Notes: Union are used extensively in the header file to allow you to describe the same memory space as one. So in the above example you can configure T1CONBITS in two ways depending on what function your are using.

## Slide 16: Typedef
C lets you define new data type names with typdef keyword. Your are not creating new data types but just new data type names.
Syntax: typedef type name;
Example:
  typedef float balance;
  balance over_due;

## Slide 17
typedef struct tagPORTABITS {
  unsigned RA0:1;
  unsigned RA1:1;
  unsigned RA2:1;
  unsigned RA3:1;
  unsigned RA4:1;
  unsigned RA5:1;
  unsigned RA6:1;
  unsigned RA7:1;
  unsigned :1;
  unsigned RA9:1;
  unsigned RA10:1;
  unsigned :1;
  unsigned RA12:1;
  unsigned RA13:1;
  unsigned RA14:1;
  unsigned RA15:1;
} PORTABITS;
extern volatile PORTABITS PORTAbits __attribute__((__sfr__));
Example of use:
PORTAbits.RA1 =1;
Notes: Extern will allow us to use it in the file that the header is included without declaring it.
Volatile tells the compiler it can change even when code has not change it.
In this example typedef is defining a new name PORTABITS to be equal to the type struct tagPORTABITS. Therefore the last line of the code makes PORTAbits an instance of the PORTABITS type, that can be used as a global variable.

## Slide 18: The if Statement
Simple form
  If (condition) statement;
  else statement; // else is optional
Block form
  If (condition)
  { //all the statements you want go here
  }
  else
  { // all the statements you want go here
  }
Notes: Note condition can be anything: if it evaluates to zero than false anything else true.

## Slide 19: Nested If
No if else in C !
An else statement always refers to the nearest if statement that is within the same block as the else and is not already associated with an if.
If(i) {
if(j) statement 1;
if(k) statement 2; //this if
else statement 3; //is associated with this else
}
else statement 4; // associated with if(i)

## Slide 20: Incrementing / Decrementing
Incrementing or decrementing by one is easy in C
The following are the same
  x = x+1; same as ++x; same as x++;
  x =x-1; same as – - x; same as x- -

## Slide 21: Incrementing / Decrementing
In an expression the order of the operator matters:
  X = 10;
  Y = ++X; //Y = 11, X=11
  But
  X=10;
  Y = X++; //Y = 10, X =11

## Slide 22: for Loops
Example of block form (single statement form exists)
For (initialization; condition; increment)
{
code to be repeated
}
Use example
int num;
for (num=1; num<1000; num++)
Notes: The code will not run if the condition is not initial met.

## Slide 23: for loop variation
Increment field can subtract or add and the increment does not have to be one.
  for(i=100; I > -100; i = i-5)
Multiple initializations and increments can be done
  for (x=0, y=0; x <= 10; ++x, --y)
Sections can be left out
  for( x=0; x!=123; ) //variation of x can come in the //loop
Infinite loop can be made for( ; ; )

## Slide 24: C Type Conversions
When variables of different types are in an arithmetic expression they are converted all to the same type.
The C compiler first makes all characters into integers and all floats are converted to doubles (this is the same thing for our compiler).
After this the compiler will promote all operands to the more precise operand
Notes: In our compiler a float and a double are the same anyways both are 32 bit respresentations.

## Slide 25: Example of Type Conversions
char ch;
int i;
float f;
double d;
result = (ch / i) + (f * d) – (f + i);
int double double
int double double
double
double
Notes: It is important to note this type conversion does not go on because of the equal sign. If result is an integer and equation is evaluated as double precision, it will try to stuff the double floating point into the integer

## Slide 26: Caution
Automatic promotion to the left side variable does not occur. A type conversion will done on the long sum of e*d but then only the lower 2 bytes will be stored in the integer
int c, e=1000;
long d=10000;
c = d*e; //c = 0x9680 should be 0x989680
Passing of variables to a function does not cause a type conversion so if you pass an unsigned int to an int it can cause and error.

## Slide 27: Cast
It is possible to force and expression to be of a specific type by using a construct called a cast
The form is: (type) expression
Unary operator
So if you wanted to force and expression to be a floating point answer you could write:
  (float) x/2

## Slide 28
Function Prototypes
When main is not the only function in the program, it is necessary to include for every function a function prototype. This is a declaration which informs the compiler the type of the function’s argument(s), if any, and its return type. It is similar to the function header seen earlier and has the same general format.
For example, the Delay10KTCYx( ) library function, described later, has the prototype shown.
The actual code of a function is called the function definition. The definition of the initialise and diagnostic functions can be seen in the Program Example 15.1 listing.
The Function Definition

## Slide 29: Prototyping of Functions
If no prototype is given and the function is defined below the use of the function then the compiler will assume the function returns an integer.
The parameter list is optional in the prototype
But if included the compiler will do stronger type checking on the number of parameters and the types
Error will be given if an illegal type conversion is needed or the argument number does not match
Notes: Parameter name is optional but lets the compiler give errors with more meaning
Illegal type conversion would be for example would be wanting a pointer and being passed a value. Caution, C does not seem to care if you pass a long double even though you declared the input to be say an integer! This can give very bad results.

## Slide 30
/*********************************************************************
Sw_to_led_18C
Runs on Derbot-18. Moves state of front microswitches to leds
Files c018i.o and p18f2420.lib are included by the Linker Script.
TJW 22.10.05 rev. 24.5.09 retested 24.5.09
**********************************************************************
Clock is 4MHz
Configuration Word all default, except: crystal oscillator (HS),
power-up timer on, brown-out detect off, WDT off, LV Program disabled*/
#include <p18F2420.h>
#include <delays.h> //header file for delays
//Function Prototypes (Library prototypes are in Header files)
void initialise (void);
void diagnostic (void);
void main (void) {
initialise(); //call initialise function
diagnostic(); //call diagnostic function
//move microswitch states to diag leds
loop:
if (PORTBbits.RB4 == 0)
PORTCbits.RC6 = 0;
else PORTCbits.RC6 = 1;
if (PORTBbits.RB5 == 0) PORTCbits.RC5 = 0; else PORTCbits.RC5 = 1;
goto loop; }
Program Example 15.1

## Slide 31
//Initialises SFRs, and sets initial outputs.
//Assumes hardware is "Build Stage 1". All unused port bits set to output.
//Mod. in App. 3 optional here, and makes no difference.
void initialise (void)
{ TRISA = 0b00000000; //All bits output (none used in this program)
TRISB = 0b00110000; //Bits 5 and 4 (microswitches) only are input
TRISC = 0b10000000; //All bits output, except bit 7 (mode switch) //Switch all outputs off
PORTA = 0;
PORTB = 0;
PORTC = 0; }
//Diagnostic: switches leds on for 1s (Tcy = 1us)
void diagnostic (void)
{ PORTCbits.RC6 = 1;
PORTCbits.RC5 = 1;
Delay10KTCYx (100);
PORTCbits.RC6 = 0;
PORTCbits.RC5 = 0;
Delay10KTCYx (100); }
Program Example 15.1 continued
Simulate Program Example 15.1 to see these points in context