## Slide 1: CPE 490 Embedded Systems
dsPIC 33 Interrupts and traps

## Slide 2: Interrupts
Interrupts allow program execution to be interrupted to respond to an event that has caused the interrupt
Useful for real time response to internal and external events
Interrupts can be used to make your own custom Real Time Operating System, instead of imposing a multitasking operating system.
Notes: To some extent the compiler manages the context switching of an ISR by inserting setup or prologue code for an ISR function. This code automatically saves the compiler-managed working and special function registers on the stack for later restoration at the end of the ISR. You can use the optional save parameter of the interrupt attribute to specify additional variables and special function registers to be saved and restored.

## Slide 3: Interrupt Overview
Each interrupt source has its own interrupt vector.
Therefore unlike the 8 bit PICs of CPE330, no need to write one grand ISR that will discover the source of the interrupt. Instead an ISR can be written separately for every interrupt source

## Slide 4
Notes: Table 7.1 of the data sheet describes each vector. Notice that this table start with the highest priority interrupt at the top and decreases as we go down the list. This interrupt table is part of the program memory space. Each space contains a 24 bit vector that describes what the ISR address is. Notice that each vector is at an even address. This is because the program memory is word addressable (the data memory is byte addressable).

## Slide 5: dsPIC33 Interrupt Overview
The architecture can support 118 different interrupt sources. The dsPIC supports 67 unique interrupt sources.
In addition there is room for 8 processor traps 5 are currently used.
7 user selected interrupt priority levels
  Interrupts with the same priority level have priority set by there vector address – the lower the address the higher the priority.
Notes: This is in contrast to the 8 bit families that have only one interrupt vector, so the interrupt Service Routine (ISR) must determine which flag is set. This allowed the ISR to scan flags in the priority order that it wants to.
Interrupt vector is location in program memory and contains an address to jump to an ISR routine.
ALTIVT allows you to use different interrupts when you are in a debug environment vs. released code. If not used the Alt table should be written to be the same as the regular table.
Unused interrupt vectors should be programmed to a address that executes a reset instruction.

## Slide 6: TRAPS Overview
A trap is a non-maskable interrupt source intended to detect hardware and software problems
Non-maskable means that all traps have a priority >7.
The priority level for each trap source is fixed. It starts at 8 and end at 15
Only one trap is assigned to a priority level.
The priority level is set by the address of the trap vector.

## Slide 7: Type of Traps
Soft traps (instruction that causes event and next instruction execute)
  DMA Error Trap (level 10 ) Both the CPU and a DMA channel attempt to write to a target address
  Math Error Trap (level 11) Divide by 0 or accumulation overflow
  Stack Error (level 12) Stack grows beyond SPLIM (Stack Pointer Limit Register) or goes below 0x0800

## Slide 8: Type of Traps
Hard Traps (only instruction that causes the trap will execute)
  Address Error (level 13) try to make a data address ending in 1, data read from an unimplemented area, or try to branch to an impossible program address.
  Oscillator Failure (Level 14)

## Slide 9: To Reset or Not that is the question
Traps by default will execute a soft reset
Traps can be written to try to recover from the error.
Traps can be written to record debugging information for reading after soft reset.

## Slide 10: Interrupt Vector Information
Every interrupt or trap has a unique source that will activate it.
Every interrupt or trap has an associated vector in a table to point to the Interrupt Service Routine (ISR)
Every interrupt (NOT traps) can be enable or disabled.
Every interrupt and trap has flag that indicates if it is active.
Every interrupt and trap has declared and implicit priority in relationship to all other interrupts.

## Slide 11: Alternate Vector table
Used for debugging
Used to try out an alternate ISR
Controlled by the ALTIVT bit in INTCON2<15>

## Slide 12: dsPIC33 External Interrupt Events
5 X External pins with level trigger detection
24 X change of state connected to GPIO (drives only one interrupt)
8 X input capture
8 X output compare
Various communication functions
Notes: External pins when they go to certain state an interrupt occurs
Change of state on GPIO, but only triggers one interrupt
Input capture is when some number of events is detected by I/O pin that starts and stops a timer
Output compare used to make a PWM signal

## Slide 13: dsPIC33 Internal Interrupts
9 X 16 bit Timers or 4 X 32 bit timers
2 X Analog to Digital Controllers
DMA used with many of the internal peripherals

## Slide 14: Interrupt Control bits
Each interrupt has 3 groups of bits associated with it.
The interrupt enable bit (IEC0-IEC4)
The interrupt flag bit (IFS0 – IFS4)
The interrupt priority level 3 bits (IPC0-IPC17)

## Slide 15: Interrupt Priority
Every interrupt can be assigned a level of priority between 0 (lowest) and 7 (highest)
Be default all priorities are set to 4. If two simultaneous interrupts occur that have the same level the order in the interrupt table sets the priority. The lowest address in the vector table has the highest priority
Traps have a priority starting at 8 and they will interrupt any other user interrupt even if nesting is disabled.

## Slide 16: Interrupt Priority Status Variables
The processor is always at an interrupt Priority level status
The priority status is kept in the status register (SR) in IPL3, IPL2, IPL1, and IPL0. At power up the level is 0.
IPL3 is only set during a trap. It can only be cleared when trying to recover from a trap. It can not be set except by a trap condition

## Slide 17: Nesting of Interrupts
Nesting: lower priority interrupts can be interrupted by higher priority interrupts.
Nesting is configurable in the INTCON1 SFR using the NSTDIS bit. If NSTDIS = 1 then nesting is disabled
  If disabled when a interrupt occurs the Interrupt Priority Level (IPL) (SR<IPL0-IPL2>) is set to 7 locking out all other interrupts.
  IPL2 though IPL0 are read only when nesting is disabled.
Notes: If nesting is disabled priority only makes sense when two or more interrupts occur simultaneously. Bits IP2 –IPL0 become read only because the processor sets the priority level to 7 any time and interrupt occurs, letting the user software rewrite these bits would defeat that purpose.

## Slide 18: What Happens During Interrupt
PC is pushed on the stack
Status register is pushed on the stack
Old CPU Interrupt priority is in the Status Register
The assembly instruction RETFIE must be executed at the end of the routine, and all the values pushed onto the stack are restored.
Notes: This is what is done automatically, the compiler will insert further code to save the context of the working registers.

## Slide 19: Stack Operation During Interrupt
Is this enough to prevent context destruction?

## Slide 20: Interrupts and the MPLAB XC16 Compiler
The compiler provides C language extensions to help you write ISRs.
By default the linker script will make sure each vector is assigned to a default ISR that just executed the RESET assembly instruction.
C functions can be an ISR as long as
  Return type is void
  No input parameters or void
  Can not be called by any other function
  Ideally they should call no other functions
Notes: We will explore how to do this in our upcoming lab.

## Slide 21: XC16 Compiler ISR
The XC16 compiler will automatically arranges for all working registers to be preserved, as well as the Status register and the Repeat Count register.
Other variables maybe saved by naming them as parameters of the interrupt attribute.

## Slide 22: XC16 Attribute Call for ISR
__attribute__((interrupt [(
[ save(symbol-list)]
[, irq(irqid)]
[, altirq(altirqid)]
[, preprologue(asm)]
)]
))
Notes: The save will allow you to push variables onto the stack, the irq and altirq will allow you to specify which vector the ISR is being written for. The preprologue lets you insert assembly level commands in the code before the function will run.

## Slide 23: Creating an ISR Function
Example :
void __attribute__((__interrupt__,__auto_psv__)) _StackError(void);
As long as you use a name for your function found is the same as in the table provided by the compiler help in MPLABX (see section 14.4 of XC16 compiler manual for instructions)

## Slide 24: C Language ISR
Remember to reset interrupt flag before exiting ISR or you will never get out of the cycle of the ISR being called.

## Slide 25: Masking Interrupts
By writing the bits IPLO-IPL2 in the SR to ones or a value of 7 this will masked all the user interrupts.
You can disable any interrupt individually by disabling it in the IECx register
Use of the DISI(n) assembly instructions, will mask up to level 6 interrupts for n instruction cycles.
Notes: The concept of a global interrupt enable in CPE 303 is gone.

## Slide 26: Bit Wise Operators
Operator | Action
& | AND
¦ | OR
^ | Exclusive OR (XOR)
~ | One’s compliment (bitwise NOT)
>> | Shift right
<< | Shift left
Notes: Compare to the logic wise operators that repeat the characters.

## Slide 27: Prototyping of Functions
If no prototype is given and the function is defined below the use of the function then the compiler will assume the function returns an integer.
The parameter list is optional in the prototype
But if included the compiler will do stronger type checking on the number of parameters and the types
Error will be given if an illegal type conversion is needed or the argument number does not match
Notes: Parameter name is optional but lets the compiler give errors with more meaning
Illegal type conversion would be for example would be wanting a pointer and being passed a value. Caution, C does not seem to care if you pass a long double even though you declared the input to be say an integer! This can give very bad results.

## Slide 28
/*********************************************************************
Sw_to_led_18C
Runs on Derbot-18. Moves state of front microswitches to leds
Files c018i.o and p18f2420.lib are included by the Linker Script.
TJW 22.10.05 rev. 24.5.09 retested 24.5.09
**********************************************************************
Clock is 4MHz
Configuration Word all default, except: crystal oscillator (HS),
power-up timer on, brown-out detect off, WDT off, LV Program disabled*/
#include <p18F2420.h>
#include <delays.h> //header file for delays
//Function Prototypes (Library prototypes are in Header files)
void initialise (void);
void diagnostic (void);
void main (void) {
initialise(); //call initialise function
diagnostic(); //call diagnostic function
//move microswitch states to diag leds
loop:
if (PORTBbits.RB4 == 0)
PORTCbits.RC6 = 0;
else PORTCbits.RC6 = 1;
if (PORTBbits.RB5 == 0) PORTCbits.RC5 = 0; else PORTCbits.RC5 = 1;
goto loop; }
Program Example 15.1

## Slide 29
//Initialises SFRs, and sets initial outputs.
//Assumes hardware is "Build Stage 1". All unused port bits set to output.
//Mod. in App. 3 optional here, and makes no difference.
void initialise (void)
{ TRISA = 0b00000000; //All bits output (none used in this program)
TRISB = 0b00110000; //Bits 5 and 4 (microswitches) only are input
TRISC = 0b10000000; //All bits output, except bit 7 (mode switch) //Switch all outputs off
PORTA = 0;
PORTB = 0;
PORTC = 0; }
//Diagnostic: switches leds on for 1s (Tcy = 1us)
void diagnostic (void)
{ PORTCbits.RC6 = 1;
PORTCbits.RC5 = 1;
Delay10KTCYx (100);
PORTCbits.RC6 = 0;
PORTCbits.RC5 = 0;
Delay10KTCYx (100); }
Program Example 15.1 continued
Simulate Program Example 15.1 to see these points in context